## Slide 1
Edge-AI Interactive Robotic Node
Low-Latency Thin-Client Architecture with Hardware-Accelerated I2S & SPI Pipelines Domain: AI in Hardware (Edge AI) Event: HACKFEST-2026 | Department of ECE, SRMIST Team: [Team Name] | Members: Member 1, Member 2, Member 3 (Dept of ECE)

## Slide 2
Abstract
• System Overview: A modular, low-power edge robotics architecture bridging physical interaction with edge/cloud intelligence.
• Distributed Paradigm: Eliminates thermal and power penalties of local edge inference by offloading models and dedicating local silicon to deterministic I/O.
• Hardware Integration: Custom carrier PCB integrating an all-digital I2S acoustic interface (INMP441/MAX98357A) and DMA-driven 40 MHz SPI display (ST7789).
• Primary Value: Demonstrates over 80% BOM reduction compared to monolithic compute systems while maintaining sub-second conversational latency.

## Slide 3
Problem Statement
• Compute & Thermal Limits: Local NLP and computer vision inference on edge SoCs cause severe thermal throttling, high idle current, and battery drain.
• Signal Integrity Issues: Conventional analog electret microphones and PWM audio output suffer from heavy EMI and ground bounce from actuator switching.
• Bus Bandwidth Bottlenecks: Standard I2C display buses (~400 kHz) achieve <1 FPS at 240x240 RGB565, causing CPU stalls and severe visual stutter.

## Slide 4
Motivation & Need
• Democratizing Physical AI: Existing companion robots cost ₹40,000+; there is a severe market need for an expressive architecture under ₹2,000.
• Hardware-Software Co-Design: Utilizing deterministic bus protocols (I2S and SPI with DMA) allows low-cost processors to run high-throughput tasks without OS jitter.
• Target Applications: Assistive desktop nodes, laboratory monitoring telemetry, and interactive smart kiosk interfaces.

## Slide 5
Proposed Solution & Architecture
• Distributed Processing: Thin-client edge node handles real-time audio/display routing, offloading heavy reasoning to a backend server.
• Acoustic Front-End (I2S): INMP441 digital MEMS microphone and MAX98357A Class-D amplifier eliminate DAC jitter and analog line noise.
• High-Speed Display Engine: 240x240 IPS panel driven over 40 MHz SPI via Direct Memory Access (DMA), sustaining 30+ FPS animation at 0% CPU load.
• Custom Carrier PCB: Altium-designed PCB featuring star grounding, matched trace lengths, and isolated power rails to prevent brownouts.

## Slide 6
Outcome & Impact
• Quantitative Latency: Achieved sub-850 ms round-trip voice-to-expression pipeline over local network infrastructure.
• Acoustic Signal Purity: High SNR maintained by keeping digital I2S traces under 30 mm and physically isolating ground planes from inductive loads.
• Economic Viability: Prototype BOM constrained under ₹2,500, with a scalable roadmap to a dedicated microcontroller board at ~₹500 in volume.
• Practical Applicability: Immediately deployable across lab environments, education robotics kits, and smart service desks.

## Slide 7
Conclusion & Roadmap
• Project Summary: Validated that a protocol-optimized thin-client architecture delivers expressive physical interaction without expensive processors.
• Milestones Completed: Schematics verified, bus timing benchmarked (I2S / SPI-DMA), and power distribution simulated.
• Round 2 Deployment: Physical PCB population, chassis mechanical integration, and live hardware demonstration at SRM campus on Oct 8-9.
• Team Contact: [teamlead_email@srmist.edu.in] | GitHub: [github.com/your-repo]